## Slide 1
DERMA PEARLS : SURGICAL PEARL - 13
Disposable cryoguard for the cryogun
Mukhtar M. surgical pearl: disposable cryoguard for cryogun. Iran J Dermatol. 2023; 26(3): 159-161.
For procuring aseptic, disposable, transparent cryoguards, disposable syringes (3 to
10ml or more) can be selected according to the diameter of lesions, and then its
barrel is cut at a length of 1 to 2 cm from the needle hub end. After this, the cut
barrel is holed (fenestrated) at 10 to 15 sites with a 16 G needle to allow the escape
of extra cryogen. Following this, the needle is separated from its hub, and the distal
part of the hub is cut to obtain a bigger and more patent hole. This needle hub is
inserted from its cut end into the nozzle of the cryogun.
Advantages of cryoguard : easy to balance the cryogun , maintains uniform distance
of 1 to 2 cm from the skin surface, cryoprobe does not get contagious as it does not
contact the skin lesions. disposable syringes are readily available, cost-effective,
aseptic &disposable. In addition, procedure is visualized due to transparency of guard.
IADVL – AP (TEAM GUNTUR)
By Dr Keerthi Sidda
Disposable cryoguards made from syringe (a), needle cap (b), centrifuge tube (c,d),or pipette (e,f).